Commercial Building Project

101 Front Street

October 13, 2010

Addendum 2

Sht A1

1.  The 19’ 0” dimension lines end at the center of the 10” block wall.

2.  The 10” interior block wall shall have drywall (painted per specs) over 1.5” metal furring strips.

3.  Interior non-load bearing walls shall be standard 3.5” metal studs.

4.  Lintel L1 mentioned in Addendum 1 Item 11 is for Window 1 & 2.

5.  All paint on interior drywall shall be acrylic latex.

Sht A3

1.  Rooms 103 and 104 shall be installed with 1/8” sheet vinyl.  The remainder of the building shall be left bare concrete with mechanical steel trowel finish.  Future tenants will choose their floor covering.  The vinyl base shall be the vertical type with no extended radius over the floor.

2.  Delete the specification for silicone spray on exterior exposed masonry surfaces.  All exterior exposed surfaces shall receive 2 coats of masonry paint as per Addendum 1.

Sht A4

1.  The 79’ 0” dimension line on the east-west length of the parking lot shall be changed to 100’ 0” to accommodate ten 10’ parking stalls on the north side.

2.  The asphalt parking lot shall be 5” of ODOT 301 Asphalt Base.  The surface of the base shall be installed 3” below the concrete walk.  An additional 1.5” of surface course shall be installed at a future date.  Walk shall slope ¼”/ft from the building.