## Slide 1: FIRE-RESISTIVE HEAVY TIMBER CONSTRUCTION

## Slide 2: History
Simple timber-framed structures appear with the oldest know civilizations.
Traditional braced frame structure: First appears in the middle ages.

## Slide 3
Contemporary timber frame construction: Used for both residential and nonresidential structures.

## Slide 4: Fire-Resistance
Large wood members have greater resistance to fire than unprotected steel.

## Slide 5
Large timbers are slow to absorb heat, slow to catch fire, and slow to burn.

## Slide 6
The charred outer layer of a partially-burned timber insulates and protects the inner portion, preserving partial structural capacity.

## Slide 7
Fire-resistive, traditional Mill Construction consists of heavy timber framing within brick masonry exterior walls.

## Slide 8
Contemporary Type IV Heavy Timber construction requires heavy timber framing within noncombustible—masonry, steel, or concrete—exterior walls.

## Slide 9: Type IV Heavy Timber
Timbers must meet minimum size requirements.
Members with lesser dimensions are classified as wood light frame (Type V) construction.
 | Supporting Floor Loads | Supporting Roof and Ceiling Loads Only
Columns | 8 x 8 (184 x 184 mm) | 6 x 8 (140 x 184 mm)
Beams and Girders | 6 x 10 (140 x 235 mm) | 4 x 6 (89 x 140 mm)
Trusses | 8 x 8 (184 x 184 mm) | 4 x 6 (89 x 140 mm)
Decking | 3 decking plus 1" finish (64 mm decking plus 19 mm finish) | 2" decking, or 1 1/8" plywood (38 mm decking, or 29 mm plywood)

## Slide 10: Type IV Heavy Timber
In IBC, allowable heights and areas for Heavy Timber buildings exceed those for unprotected steel (Type IV-B).

## Slide 11: Type IV Heavy Timber
…and roughly equal those for steel, concrete, or masonry with 1-hour of fire protection (Type IV-A).

## Slide 12: Managing Wood Shrinkage
Different rates of shrinkage between interior wood framing and exterior masonry, steel, or concrete walls can lead to differential settling of upper floors and roofs.
Wood connection details should minimize the cumulative effects of cross-grain shrinkage.

## Slide 13: Traditional cast iron pintle
Upper-story columns are isolated from cross-grain shrinkage in wood beams and girders at each floor level.

## Slide 14: Contemporary Connections
Columns should not bear on beams or girders, so that they are unaffected by shrinkage in the floor frame.
In this example, column is continuous.

## Slide 15
Example use of split-ring connectors (greater bearing capacity than bolted connections)

## Slide 16: Beam/Wall Anchorage
Traditional fire cut beam ends: Prevent collapse of wall in event of beam failure in fire.

## Slide 17
A ventilating air space around the beam end prevents moisture in the masonry wall from seeping into the beam.

## Slide 18
Upper clip restrains beam from side-to-side movement while allowing rotation due to structural deflection or beam collapse in a fire.

## Slide 19: Floor and Roof Decks
Heavy decking comes in depths of 2" to 8", capable of spanning roughly from 5' to more than 20'.
To achieve the required fire-resistance, floor decking must be covered with tongue-and-groove boards or plywood.

## Slide 20
Concealed combustible spaces, where fire could develop undetected must be avoided.

## Slide 21: HEAVY TIMBER IN OTHER CONSTRUCTION TYPES

## Slide 22: Type V Construction
When HT is used in Type V construction, it is subject to this Type’s reduced height and area limits.
(Type V construction permits combustible members of any size and combustible exterior walls.)

## Slide 23: Heavy Timber Roof Framing
HT roof framing is permitted in any construction type requiring no more than a 1-hour fire-resistance rating.
For example, heavy timber framing can substitute for 1-hour protected steel or concrete roof framing in Type I and II noncombustible buildings.

## Slide 24: LATERAL BRACING

## Slide 25: Knee Bracing
Stiffens column/beam connection and adds lateral stiffness to the heavy timber frame.

## Slide 26: Full-Bay Cross Bracing
Provides greater lateral stiffness and strength.
(Wood or steel)

## Slide 27: Shear Walls
Masonry or concrete walls can act as shear walls to provide lateral stability.

## Slide 28: Structural Wood Panels
Panels attached to the frame act as shear walls.

## Slide 29: CROSS-LAMINATED TIMBER CONSTRUCTION

## Slide 30
Fabricated panels are shipped to construction site then lifted into place.

## Slide 31
Simple connection hardware

## Slide 32
Simple assembly concepts.
Panels can act as loadbearing walls, floors, and roof decks.

## Slide 34
Low weight/high strength
2-way structural capacity
Rapid assembly
Minimal construc-tion site waste
Negative carbon footprint
Design: DI Ulli Koller, Ing. Thomas Stiegler

## Slide 35: Exposed Services
Without concealed spaces, power, lighting, ductwork, sprinklers, and other services frequently are routed in the open.

## Slide 36: CONNECTIONS

## Slide 37
Traditional, pegged, mortise and tenon joinery

## Slide 38
Proprietary fastening system with self-drilling steel dowels and concealed steel plates

## Slide 39
Fabricated steel seat, concealed plates, and exposed through-bolts

## Slide 40
Steel plate gusset with tie rod and through-bolts

## Slide 41
Copper sheet metal flashing protects the open-grain ends of beams and columns from absorbing moisture

## Slide 42: LONGER SPANS IN HEAVY TIMBER

## Slide 43: Large Beams
Glulam beams can span over 80', and arches even further.

## Slide 44: Trusses
Heavy timber trusses can span beyond 200'.

## Slide 45: Domes
The Washington State Tacoma Dome spans 530'.

## Slide 46: Metropol Parasol, Seville
Covers area 490’ by 245’