## Slide 1: PLATFORM FRAME

## Slide 2: Balloon Frame
Small-dimension members span from ground floor to roof.
North-American invention
Light wood frame uses lighter wood members, simpler nailed connections
Requires less skilled builders

## Slide 3
Precursor technologies:
Water- or steam-powered saw mills
Machine-made nails
Railroad transportation

## Slide 4: Platform Frame
Relies on shorter length, single-story height members that are easier to produce, handle, and erect.

## Slide 5: Platform Framing
Platform…walls…platform…walls…

## Slide 6
Nominal 2-inch members
Spaced at 16" or 24"
Floor, ceiling joists
Wall studs
Roof rafters

## Slide 7
Panels applied over framing:
Floor subflooring
Wall and roof sheathing
OSB, plywood, or other material

## Slide 8: FOUNDATIONS FOR LIGHT FRAME STRUCTURES

## Slide 9: Residential Basement Foundation
Excavation to necessary depth of basement (and at least below the frost line)

## Slide 10
Cast-in-place concrete strip footing
Cast-in-place concrete foundation wall, 8" to 12" thick, 8' to 10' tall

## Slide 11
Section
Anchor bolts cast into top of wall
Steel reinforcing top and bottom of wall

## Slide 12
Dampproofing or waterproofing on outside of wall
Crushed stone and perforated perimeter drain

## Slide 13
Backfill, after floor platform is erected and can brace walls.
Slab on grade may be delayed until structure is closed in.

## Slide 14: Foundation Insulation
Exterior: Usually board type, resistant to moisture and insects
Interior: Many types; some must be protected from fire.

## Slide 15
Crawlspaces may be ventilated to the exterior or treated as interior conditioned space.

## Slide 16
Cast-in-place concrete foundation wall with anchor bolts protruding
Note pockets in far side of concrete wall for setting of floor beams.

## Slide 17
Exterior foundation insulation: Expanded polystyrene rigid foam

## Slide 18: BUILDING THE FRAME

## Slide 19: Ground Floor Platform
Sill plates anchored
Girders placed
Floor joists laid
Subflooring applied

## Slide 20
Section
Sill plates anchored
Girders placed
Floor joists laid
Subflooring applied

## Slide 21
Preservative-treated 3x8 sill plate with closely spaced anchor bolts

## Slide 22
Oversized square washers create a stronger sill-to-foundation connection, for resistance to seismic forces.

## Slide 23
Floor framing with 2x12 solid member joists

## Slide 24
Wall sections are assembled lying down, then tilted into place.
Temporary bracing holds walls in alignment.

## Slide 25
Wall sheathing may be applied before the walls are stood up, or later, after the frame is fully erected (as shown here).

## Slide 26
Section:
Bottom plates nailed to floor platform
Studs continuous between top and bottom plates

## Slide 27
Top plates are doubled, to support joists or rafters above.
Plates ends are staggered to tie separate wall sections together.

## Slide 28: Steps in Framing a Wall
Layout

## Slide 29
Studs at special locations for openings and corners are inserted first.

## Slide 30
Regular studs spaced at 16” or 24” o.c. are filled in.

## Slide 31
Diagonal bracing or rigid sheathing is applied.

## Slide 32
Framing at corners provides nailing surfaces for interior wallboard and exterior sheathing.

## Slide 33: Rough Opening
Jack studs support the header.
The header supports the loads above the opening.

## Slide 34
Walls are constructed in sections, lying down on the floor platform and then tilted up into position.

## Slide 35
Adjustable, bowed springboards allow precise alignment of the walls.

## Slide 36
Window rough opening, viewed from the inside, with the window installed.

## Slide 37
Bottom section of sheathing is preservative treated plywood, to protect from decay at raised grade on exterior side.
Upper portion is OSB.

## Slide 38
Glulam beam spans large garage door opening.

## Slide 39: Lateral Force Resistance
Sliding
Overturning
Wracking
Failure among among parts

## Slide 40
Anchor bolts resist sliding.

## Slide 41
Hold-downs resist overturning.
(Will be nailed over sheathing after sheathing is applied).

## Slide 43
Shear walls resist wracking:
Plywood sheathing

## Slide 44
With high lateral forces, special nailing is required to ensure adequate load transfer.

## Slide 45
Any solid sheathed area may act as a shear wall.
Interior walls, properly constructed, can also act as shear walls.

## Slide 46
Higher strength prefabricated assemblies may be used where solid wall area is limited.

## Slide 47
Metal strapping is one form of collector used to transfer forces between parts.

## Slide 48: Upper Floor Platform
Upper floor framing much the same as ground floor.

## Slide 49
Section
Rim joists and interior blocking close off joist spaces and prevent the joists from tipping.

## Slide 50
With I-joists, the thinber webs require stiffeners, blocking, or squash blocks to support loads from above.

## Slide 51
I-joist framing seen from below.
Note web stiffeners at joist ends.

## Slide 52
I-joist framing seen from above.

## Slide 53: Upper Floor Walls
Each floor platform makes a convenient work surface for building the next set of walls.

## Slide 54: Roof Framing
Ceiling joists and roof rafters are erected on top of the upper floor walls.

## Slide 55
A knowledgeable framer can lay out all cuts on a sloped rafter with nothing more than a traditional framing square and pencil.

## Slide 56
Collar ties, close to the upper ends of the rafters, resist wind uplift forces.
Ceiling joists, close to the lower ends of rafters, resist the rafter horizontal spreading forces that could cause the walls to spread outward.

## Slide 57
Solid lumber rafters in a gable roof and dormer.

## Slide 58
When rafters are not tied at the lower ends, a structural ridge beam (steel in this example) is required to prevent the ridge from sagging and the rafters from pushing outward on the tops of the walls.

## Slide 59
The complex cuts required for hip or valley framing can also be laid out with just a framing square.

## Slide 60
Pre-fabricated roof trusses with temporary bracing

## Slide 61
A fully framed and sheathed structure.
Finish carpentry work at the roof eaves has begun.